Multimedia Group

TEST PLAN

Draft Version 1.3

June 18, 2004

Contact:	D. Hands	Tel: 	+44 (0)1473 648184

Fax: 	+44 (0)1473 644649

E-Mail: david.2.hands@bt.com

Editorial History

| Version | Date | Nature of the modification |
| --- | --- | --- |
| 1.0 | July 25, 2001 | Initial Draft, edited by H. Myler |
| 1.1 | 28 January, 2004 | Revised First Draft, edited by David Hands |
| 1.2 | 19 March, 2004 | Text revised following VQEG Boulder 2004 meeting, edited by David Hands |
| 1.3 | 18 June 2004 | Text revised during VQEG meeting, Rome 16-18 June 2004 |

Summary

List of Acronyms

1. Introduction	6

2. Subjective Evaluation Procedure	7

2.1.The <<XXX>> method	7

2.1.1.General description	7

2.1.2.Viewing conditions	7

2.1.3.Instructions to viewers for quality tests	7

2.1.4.Viewers	7

2.2.Data format	7

2.2.1.Results data format	7

2.2.2.Subject data format	7

2.2.3.Subjective Data analysis	7

3.Test Laboratories	7

3.1.ILG	7

3.2.Proponent Laboratories	7

4.Sequence processing and data formats	8

4.1.Sequence processing overview	8

4.2.Test materials	8

4.2.1.Selection of test material (SRC)	8

4.2.2.Hypothetical reference circuits (HRC)	8

4.2.3.Distribution of tests over facilities	8

4.2.4.Processing and editing sequences	8

4.2.5.Randomization	8

4.2.6.Presentation structure of test material	8

5.Objective Quality Models	8

5.1.Model type	8

5.2.Model input and output data format	8

5.3.Submission of executable model	8

5.4.Registration	9

5.5.Results analysis	9

6. Objective quality model evaluation criteria	10

6.1.Introduction to evaluation metrics	10

6.2.Evaluation Metrics	11

6.2.1.Metrics relating to Prediction Accuracy of a model	12

6.2.2.Metrics relating to Prediction Monotonicity of a model	12

6.2.3.Metrics relating to Prediction Consistency of a model	12

6.2.4.Metrics relating to agreement	13

6.3.Generalizability	13

6.4.Complexity	14

7.Calendar and actions 	14

8. Recommendation	14

9.Bibliography	15

10.Annex: Optimum mean square quantization method.	15

10.1.The Lloyd Iteration for codebook improvement	15

10.2.The Lloyd algorithm	16

List of Acronyms

ACR-HRR	Absolute Category Rating with hidden reference removal

ANOVA	ANalysis Of VAriance

ASCII	ANSI Standard Code for Information Interchange

CCIR	Comite Consultatif International des Radiocommunications

CODEC	Coder-Decoder

CRC	Communications Research Center (Canada)

DVB-C	Digital Video Broadcasting-Cable

FR	Full Reference

GOP	Group of Pictures

HRC	Hypothetical Reference Circuit

IRT	Institut Rundfunk Technische (Germany)

ITU	International Telecommunications Union

MM	multimedia

MOS	Mean Opinion Score

MOSp	Mean Opinion Score, predicted

MPEG	Motion Pictures Expert Group

NR	No (or Zero) Reference)

NTSC	Nat’l Television Standard Code (60 Hz TV)

PAL	(50 Hz TV)

PS	Program Segment

QAM	Quadrature Amplitude Modulation

QPSK	Quadrature Phase Shift Keying

RR	Reduced Reference

SMPTE	Society of Motion Picture and Television Engineers

SRC	Source Reference Channel or Circuit

SSCQE 	Single Stimulus Continuous Quality Evaluation

VQEG	Video Quality Experts Group

VTR	Video Tape Recorder

# Introduction

This document defines the procedure for evaluating the performance of objective perceptual quality models submitted to the Video Quality Expert Group (VQEG) formed from experts of ITU-T Study Groups 9 and 12 and ITU-R Study Group 6. It is based on discussions from various meetings of the VQEG Multimedia working group (MM), on 6-7 March in Hillsboro, Oregon at Intel and on 27-30 January 2004 in Boulder, Colorado at NTIA/ITS.

The goal of the MM group is to recommend a quality model suitable for application to digital video quality measurement in multimedia applications. Multimedia in this context is defined as being of or relating to an application that can combine text, graphics, full-motion video, and sound into an integrated package that is digitally transmitted over a communications channel. Common applications of multimedia that are appropriate to this study include video teleconferencing, video on demand and Internet streaming media. The measurement tools recommended by the MM group will be used to measure quality both in laboratory conditions using a FR method and in operational conditions using RRNR methods.

In the first stage of testing, it is proposed that video only test conditions will be employed. Subsequent tests will involve audio-video test sequences and eventually true multimedia material will be evaluated. It should be noted that presently there is a lack of both audio-video and multimedia test material for use in testing. Video sequences used in VQEG Phase I remain the primary source of freely available (open source) test material for use in subjective testing. The VQEG does desire to have copyright free (or at least free for research purposes) material for testing. The capability of the group to perform adequate audio-video and multimedia testing is dependent on access to a bank of potential test sequences.

The performance of objective models will be based on the comparison of the MOS obtained from controlled subjective tests and the MOSp predicted by the submitted models. This testplan defines the test method or methods, selection of test material and conditions, evaluation metrics to examine the predictive performance of competing objective multimedia quality models.

The goal of the testing is to examine the performance of proposed video quality metrics across representative transmission and display conditions. To this end, the tests will enable assessment of models for mobile/PDA and broadband communications services. It is considered that FR TV and RRNR TV VQEG testing will adequately address the higher quality range (2 Mbit/s and above) delivered to a standard definition monitor. Thus, the Recommendation(s)  resulting from the VQEG MM testing will be deemed appropriate for services delivered at 2 Mbit/s or less presented on mobile/PDA and computer desktop monitors.

It is expected that subjective tests will be performed separately for different display conditions (e.g. one specific test for mobile/PDA; another test for desktop computer monitor). The performance of submitted models will be evaluated for each type of display condition. Therefore it may be possible for one model to be recommended for one display type (say, mobile) and another model for another display format (say, desktop monitor).

The objective models will be tested using a set of digital video sequences selected by the VQEG MM group. The test sequences will be processed through a number of hypothetical reference circuits (HRC's). The quality predictions of the submitted models will be compared with subjective ratings from human viewers of the test sequences as defined by this Test Plan.

A final report will be produced after the analysis of test results.

# Subjective Evaluation Procedure

## The ACR (with hidden reference removal) method

This section describes the test method according to which the VQEG MM subjective tests will be performed.

### General description

The selected test methodology is the single stimulus Absolute Category Rating method  with hidden reference removal (henceforth referred to as ACR-HRR). This choice has been selected due to the fact that ACR provides a reliable and standardised method (ITU-R Rec. 500-11, ITU-T P.910) that allows a large number of test conditions to be assessed in any single test session

In the ACR test method, each test condition is presented once only for subjective assessment. The test presentation order is randomized according to standard procedures (e.g. Latin or Graeco-Latin square). The test format is shown in XXX. At the end of each test presentation, subjects provide a quality rating using the ACR rating scale (see XXX).

Figure 1 – ACR basic test cell

### Application Across Different Video Formats and Displays

The proposed MM test will examine the performance of objective perceptual quality models for different video formats (Rec. 601, CIF and QCIF) presented on different displays (simulated mobile and desktop monitor). Section 4 defines format and display types in detail. It is proposed that two types of subjective tests will be performed, one using a simulated mobile platform for QCIF and CIF formatted video; the other test will employ some standard desktop monitor for Rec. 601 formatted video. For both mobile and desktop tests the ACR method will be applied.

Presently, VQEG MM assumes a rolling programme of tests. The first test will focus on video; with future tests examining audio-video. The audio-video tests may involve three separate stages. Stage 1 will assess video quality only. Stage 2 will assess audio quality only. Stage 3 will assess overall (audio-video_ quality. All three stages will apply the ACR method. For audio and audio-video tests, the room must be acoustically isolated and conform to relevant international standards (e.g. ITU-T Rec. P.800. and ITU-R Rec. BS.1116). Use of headphones will be investigated and perhaps included or mandated in the test (e.g., Stax diffused field equalized Headphones). The specification and selection of audio and video cards is to be decided.

The instructions given to subjects will require subjects to maintain a specified viewing distance from the display device. The viewing distance has been agreed as:

- QCIF: nominally 6-10H and let viewer choose within physical limits (natural for PDAs).

- CIF:	6-8H and let viewer choose within physical limits.

- Rec. 601:	6H

H=Picture Heights (picture is defined as the size of the video window)

### Display Specification and Set-up

Given that the subjective tests will use LCD displays it is necessary to ensure that each test laboratory selects appropriate display specification and common set-up techniques are employed. VQEG MM will require that LCD displays meet the following specifications:

The LCD should be set-up using the following procedure:

- Use the autosetting to set the default values for luminance, contrast  and colour shade of white

- Adjust the brightness according to Rec. ITU-T P.910, but do not adjust the contrast (it might change balance of the colour temperature).

- Set the gamma to 2.2

Set the colour temperature to 6500 K (default value on most LCDs)

The LCD display should be selected as high-quality monitor that it could be verified that different display of same model and brandname uses the same panel inside either from the display manufacturer or through the TCO-testing labs, e.g. Eizo ColorEdge. The LCD display that is selected should have a similar pixel pitch as currently available PDAs and mobile phones.

This set-up procedure may be modified following the work of the VQEG subjective test set-up group.

### Viewers

Each test will require at least 24 subjects to comply with ITU-R Rec. 500. It is recommended that as many subjects as possible participate in each test in order to improve the statistical power of the resulting data. The viewers will be assigned to sub-groups, which will see the test sessions in different orders (Section X.X).

Only non-expert viewers will participate. The term non-expert is used in the sense that the viewers’ work does not involve television picture quality and they are not experienced assessors. They must not have participated in a subjective quality test over a period of six months. All viewers will be screened prior to participation for the following:

- normal (20/20) visual acuity with or without corrective glasses (per Snellen test or equivalent)

- normal colour vision (per Ishihara test or equivalent)

- familiarity with the language sufficient to comprehend instruction and to provide valid responses using semantic judgement terms expressed in that language.

Note; for any test involving audio, appropriate screening for normal hearing should be applied (following relevant audio test recommendations).

### Viewing Conditions

Each test session will involve only one subject assessing the test material. Subjects will be seated directly in line with the centre of the video display at the appropriate viewing distance. The test cabinet will conform to ITU-R Rec. 500 requirements for ambient lighting.

### Test data collection

The collection and organization of the data files containing the votes will be under the direct responsibility of the ILG Chair.

## Data Format

### Results Data Format

### Subject Data Format

### Subjective Data Analysis

Each subject's results will be checked for completeness. An observer is discarded if the number of failed votes exceeds one in one of the sessions. Additionally, the observers will be screened after the test as specified in sec. 2.3.1 of Annex 2 “Screening for DSIS, DSCQS and alternative methods except SSCQE method” of recommendation ITU-R BT.500-10. The post-test screening will not be applied to these sub-groups but to the groups which participate in one test as a whole.

Following convention when using the DSCQS, difference scores will be calculated. The difference scores, known as Difference Mean Opinion Scores (DMOS) will be produced for each test condition. Difference scores will be used to assess the performance of each full reference and reduced reference proponent model, applying the metrics defined in Section 5.

For evaluation of no reference proponent models, the absolute (raw) subjective score will be used. Thus, for each DSCQS reference-test pairing, only the absolute rating for the test condition will be calculated. Based on each subject's absolute rating for the test presentations, an absolute mean opinion score will be produced for each test condition. These MOS will then be used to evaluate the performance of NR proponent models using the metrics specified in Section 6.

# Test Laboratories and Schedule

Given the scope of the MM testing, it is proposed that both independent test laboratories and proponent laboratories will be given subjective test responsibilities. The ILG will oversee the testing to ensure that all laboratories conform to the requirements set out in this testplan.

## ILG

The independent test group is composed of FUB (Italy), CRC (Canada) and Verizon (USA). A proposal from France Telecom has been received where FT would become an ILG. However, FT will only act as a member of the ILG if the MSCQS method is included in the subjective testing process. Currently, it has been provisionally agreed for FT to participate using the MSCQS method, but that the results from this method would only be valid if they mirror results from laboratories using the DSCQS approach. FT would receive a reduced fee for acting as an independent test laboratory.

## Proponent Laboratories

A number of proponents also have significant expertise in and facilities for subjective quality testing. Proponents indicating a willingness to participate as test laboratories are BT, Genista, NTIA, NTT, and Opticom and Yonsei. Precise details of how proponent laboratories would create test material and distribute results from their tests have yet to be specified. It is clearly important to ensure all test data is derived in accordance with this testplan. Critically, proponent testing must be free from charges of advantage to one their model or disadvantage to competing models.

## Test schedule

TABLE 1:  Below is the list of actions and the associated schedule.

| Action | Done by | Source | Destination |
| --- | --- | --- | --- |
| Testplan completed and approved | 8 November 2004 | VQEG | VQEG Reflector, ITU |
| Final HRCs and SRCs agreed | By end of October 2004 meeting, | ILG | VQEG Reflector, ITU |
| Call for proponents to submit models (ITU-R, ITU-T) | May 2004 | WP6Q SG9, SG 12 | Proponents |
| Final submission of executable model | End of testplan + 6 months | Proponents | ILG |
| Fee payment | End of testplan + 4 months | Proponents | ILG |
| Declaration by proponents submitting model(s); proponents identify type of model to be submitted | End of testplan + 1 month | Proponents | VQEG |
| List of proponent models submitted for evaluation | Fee payment + 1 week | VQEG co-chairs | VQEG |
| Delivery of HRC video material | End 2004 | Proponents | ILG |
| Delivery of selected test material to be used in subjective tests | Final submission of executable models + 1 month | ILG | Proponents |
| Completion of Formal Subjective Tests | 3 months after test sites have receiving test material | Test sites | Test sites |
| Delivery of objective data | 3 months after proponents have received test material | Proponents | Proponents and ILG |
| Verification of submitted models | 1 month after subjective and objective data becomes available | Proponents | ILG |
| Statistical analysis (according to statistics defined in Section 6 of the testplan) | 1 month after subjective and objective data becomes available | VQEG | VQEG |
| Final report | 1 month after statistical analysis has been completed | VQEG | WP6Q SG9 SG12 |
| VQEG/JRG MMQA meeting to discuss final report | Soon after final report becomes available | VQEG | VQEG |

The ILG will verify that the submitted models (1) run on the ILG’s computers and (2) yield the correct output values when run on the test video sequences. Due to their limited resources, the ILG may encounter difficulties verifying executables submitted too close to the model submission deadline.  Therefore, proponents are strongly encouraged to submit a prototype model to the ILG the verification deadline, to work out platform compatibility problems well ahead of the final verification date.  Proponents are also strongly encouraged to submit their final model executable 14 days prior to the verification deadline date, giving the ILG two weeks to resolve problems arising from the verification procedure.

The ILG requests that proponents kindly estimate the run-speed of their executables on a test video sequence and to provide this information to the ILG.

# Sequence Processing and Data Formats

Three subjective tests will be performed. The first test will assess the subjective quality of video material presented on a simulated mobile environment. This test will deploy a LCD monitor and present video in QCIF (176x144 resolution). The second test will present CIF (352x288 resolution) video. The third test will use Rec. 601 format (720 x 576 resolution) video.

Note that in all subjective tests 1 pixel of video will be displayed as 1 pixel native display. No upsampling or downsampling of the video is allowed.

Presently, VQEG has access to a set of video test sequences. For audio-video tests this database needs to be extended to include new source material containing both audio and video.

## Sequence processing overview

The test material will be selected from a common pool of video sequences. If the test sequences are in interlace format then a standard, agreed de-interlacing method will be applied to transform the video to progressive format. All source material should be 25 or 30 frames per second progressive except for animation. The de-interlacing algorithm will de-interlace Rec. 601 formatted video into 525 line and 625 line progressive video at 30 fps and 25 fps respectively, as well as producing CIF and QCIF formats.  Algorithms will be proposed on the VQEG reflector and approved before processing takes place. Uncompressed AVI files will be used for subjective and objective tests.  Tools are being sought to convert from the various coding schemes to uncompressed AVI. Video (full frame, full frame rate) and audio (16 bit, 44-48 kHz stereo) interleaved each frame (if audio-video material is available). The progressive test sequences used in the subjective tests should also be used by the model's to produce objective scores.

The source test material should be in Rec. 601, DigiBeta, Betacam SP, or DV25 (3-chip camera) format or better. Note that this requirement does not apply to Categories 4 and 8 (Section 4.2) where the best available quality reference will be used.

VQEG MM expresses a preference for all test material to be open source.

## Test materials

The test material will be representative of a range of content and applications. The list below identifies the type of test material that form the basis for selection of sequences.

1)	video conferencing (available, NTIA (Rec 601 60Hz); BT to provide more (Rec 601 50Hz), Yonsei (QCIF), FT (Rec 601 50Hz))

2)	movies, movie trailers (VQEG Phase II?)

3)	sports, (available, + 15-20 mins from Yonsei, + Comcast)

4)	music video,

5)	advertisement, (Logitech)

6)	animation (graphics Phase I, cartoon Phase II; Opticom possible, NTIA possible)

7)	broadcasting news (more on the news, not on the studio).  (available – Yonsei; possible Comcast)

home video (FUB possibly, BT possibly)

### Selection of test material (SRC)

Selection of test material will be done by the ILG. Proponents will be asked to provide source material as well as SRC/HRC combinations for consideration by the ILG when selecting test conditions for the subjective tests. The test should include some agreed percentage (e.g. 20%) of new SRC/HRC combinations that are unknown to proponents. The ILG will be responsible for selection of this unknown test material.

Further guidelines on selection of and access to test material are required if proponents are to be test laboratories.

## Hypothetical reference circuits (HRC)

The subjective tests will be performed to investigate a range of HRC error conditions. These error conditions may include, but will not be limited to, the following:

- Compression errors (such as those introduced by varying bit-rate, codec type, frame rate and so on)

- Transmission errors

- Post-processing effects

The overall selection of the HRCs will be done such that most, but not necessarily all, of the following conditions are represented:

### Video bit-rates:

- PDA/Mobile: 	16kbs to 320 kbs (e.g., 16, 32, 64, 128, 192, 320)

- PC1 (CIF):		128kbs to 704kbs (e.g. 128, 192, 320, 448, 704)

- PC2 (601):		320kbs to 2Mbs (e.g. 320, 448, 704, ~1M, ~1.5M, ~2M)

### Transmission Errors

Error conditions produced using packet loss rates and bit errors:

- Level 1: 		None

- Level 2:		Low

- Level 3		Medium

- Level 4:		High

Proponents are asked to provide examples of error conditions that are relevant to the industry.  These examples will be viewed at the next meeting and/or examined after electronic distribution (only open source video is allowed for this).  Error conditions can be introduced using packet-loss and/or bit error conditions.

When producing test material, care must be taken to ensure that the codec has stabilized before the actual test sequence begins and after it has ended (e.g. if using VQEG Phase I material, concatenation of the sequence with parts of itself would probably be required).

### Frame Freezing and Frame Skipping

A frame freeze is defined as any event where the video pauses for some period of time then restarts without losing any video information. The temporal delay through the system increases. Frame freezes will not be included in the current testing.

Frame skipping is defined as events where the video pauses then restarts with some loss of video information. In frame skipping, the temporal delay through the system is approximately unchanged. Anomalous frame skipping (*definition required*) is not allowed during the first 1s or the final 1s of a video sequence. Note that where skipping is included in a test then source material containing still sections should form part of the testing.

### Frame rates

For those codecs that only offer automatically set frame rate, this rate will be decided by the codec. Some codecs will have options to set the frame rate either automatically or manually. For those codecs that have options for manually setting the frame rate (and we choose to set it for the particular case), 5 fps will be considered the minimum frame rate (an exception might be made for the PDA/mobile test).

Manually set frame rates (new-frame refresh rate) may include:

- PDA/Mobile: 	30, 25, 15, 10, 5, 2.5 fps

- PC1 (CIF):		30, 25, 15, 10, 5 fps

- PC2 (601):		30, 25, 15, 10, 5 fps

Temporally varying frame rates are acceptable for the HRCs

Care must be taken when creating test sequences for display on a PC monitor. The display refresh rate can influence the reproduction quality of the video and VQEG MM requires that the sampling rate and display output rate are identical. For example,

Given an initial Frame rate of video is 30fps, the sampling rate is 30/X (e.g.  30/2 = sampling rate of 15fps). This is called frame rate. Then we upsample and repeat frames from the sampling rate of 15fps to obtain 30 fps for display output.

### VQEG MM must agree on a scan rate for PC monitors prior to test (e.g. 50Hz, 60Hz, 75Hz, etc).

### Pre-Processing

The HRC processing  may include, typically prior to the encoding, one or more of the following:

- Filtering

- Simulation of non-ideal cameras (e.g. mobile)

- Colour space conversion (e.g. from 4:2:2 to 4:2:0)

This processing will be considered part of the HRC.

### Post-Processing

The following  post-processing effects may be used in the preparation of test material:

- Colour space conversion

- De-blocking

- Decoder jitter

### Coding Schemes

Coding Schemes that will be used may include, but are not limited to:

- Windows Media Player 9

- H.263

- H.264 (MPEG-4 Part 10)

- Real Video (e.g. RV 10)

- MPEG 4

### Distribution of tests over facilities

### Processing and editing sequences

Test sequences will be captured from the decoded video in uncompressed format. Two capture methods may be employed. The two methods are as follows:

The captured video file should be in AVI container.

### Randomization

### Presentation structure of test material

# Objective Quality Models

## Model type

VQEG MM has agreed that Full Reference, Reduced Reference and No reference models may be submitted for evaluation. The sidechannel allowable for the RR models are:

- PDA/Mobile (QCIF): 	(1k, 10k)

- PC1 (CIF):		(10k, 64k)

- PC2 (601):		(10k, 64k, 128k)

Proponents may submit one model of each type for all image size conditions. Thus, any single proponent may submit up to a total of 13 different models. Note that where multiple models are submitted, additional model submission fees may apply.

## Model input and output data format

## Submission of executable model

## Registration

Full Reference Models must include calibration.

Reduced-Reference Models must include temporal calibration if the model needs it. Temporal misalignment of no more than +/-0.25s is allowed. Please note that in subjective tests, the start frame of both the reference and its associated HRCs are matched as closely as possible. Spatial offsets are expected to be very rare.  Spatial registration will be assumed to be within (1) pixel. Gain, offset, and spatial registration will be corrected, if necessary, to satisfy the calibration requirements specified in this test plan.

No-Reference Models should not need calibration

## Results analysis

# Objective quality model evaluation criteria

Data Analysis

The same techniques that were used in the VQEG PhaseII test and reported in the final report will be used.

If DSCQS, need to include F-tests and consider aggregation issues.

## Introduction to evaluation metrics

A number of attributes characterize the performance of an objective video quality model as an estimator of video picture quality in a variety of applications. These attributes are listed in the following sections as:

- Prediction Accuracy

- Prediction Monotonicity

- Prediction Consistency

This section lists a set of metrics to measure these attributes. The metrics are derived from the objective model outputs and the results from viewer subjective rating of the test sequences. Both objective and subjective tests will provide a single number (figure of merit) for each half second of the processed sequence that correlates with the video quality MOS of the processed sequence. It is presumed that the subjective results include mean ratings and error estimates that take into account differences within the viewer population and differences between multiple subjective testing labs.

The objective quality model evaluation should be done in 5 steps, as described below. Two main evaluations are proposed, one common evaluation, and a post processed evaluation. The post processed evaluation allows an increase in the number of evaluation criteria in a meaningful way. The quantized evaluation is often more relevant than other comparisons.

| 1 | Data set verified by ILG. |
| --- | --- |
| 2 | Evaluation Metrics for the data set |
| 3 | Post processing : quantization |
| 4 | Evaluation Metrics for the quantized data set |
| 5 | Diagnostic |

Objective quality model evaluation.

Evaluation metrics are described below and several metrics are computed to develop a set of comparison criteria. Furthermore, the data set should not be shared to keep information secure. Thus, if a proponent wanted to share the data set to distinguish several reduced reference bitrate categories, or other specific aspects, it will have to be discussed before the data analysis starts. The data set parts will have to be large enough to allow relevant statistical analysis (at least 600 MOS corresponding to one segment). Finally, all data parts will be size equivalent, and have the same standard deviation, to be compared each other.

Summary of evaluation criteria:

| Common criteria | Criteria for quantized data |
| --- | --- |
| Metric 1 | 95 % confidence interval | Metric 1 | 95 % confidence interval |
| Metric 2 | Root mean square error | Metric 2 | Root mean square error |
| Metric 3 | Pearson linear correlation | Metric 3 | Spearman Rank order correlation |
| Metric 4 | Outlier ratio | Metric 4 | Outlier ratio |
| Metric 5 | Kurtosis | Metric 5 | Kurtosis |
|  |  | Metric 6 | Kappa coefficient |

## Evaluation Metrics

This section lists the evaluation metrics to be calculated on the subjective and objective data. Once the nonlinear transformation (see Section X) section has been applied to subjective and objective data, the objective model prediction performance is then evaluated by computing various metrics on the actual sets of data.

The set of differences between measured and predicted MOS is defined as the quality-error set Qerror[]:

Qerror[i] = MOS[i] – MOSp[i]

Where the index i refers to a Time Code of the processed video sequence.

### Metrics relating to Prediction Accuracy of a model

Metric 1:	The 95% inverse-confidence interval-weighted root-mean-square error of the error set Qerror[].

with CONF[i] = 95% confidence interval for the ith point (of N points). The constant factor of 0,5 is added to stabilize the calculation for cases of very small confidence interval.

Metric 2:	The simple root-mean-square error of the error set Qerror[].

Note: The usual Pearson linear correlation coefficient between MOSp and MOS will not be used for quantized data due to the large amount of data where the Pearson correlation becomes inefficient. Instead, the Spearman rank order correlation will be used, which is well adapted for quantized data.

### Metrics relating to Prediction Monotonicity of a model

Metric 3:

For quantized data: Spearman rank order correlation coefficient between MOSp and MOS.

Therefore, results obtain with this metric must be interpreted carefully. Thus, there is a lot of data and only 5 possible values, so there is a very large amount of ex-æquo ???<<XXX>>. When the ex-æquo proportion is too large, the metric becomes less efficient; so the results can’t be considered alone. This metric has to be taken into account with regard of others metrics.

For classical data: Pearson linear correlation between MOS and MOSp.

### Metrics relating to Prediction Consistency of a model

Metric 4: 	Outlier Ratio of “outlier-points” to total points N.

Outlier Ratio = (total number of outliers)/N

where an outlier is a point for which: ABS[ Qerror[i] ] > 2*MOSStandardError[i].

Twice the MOS Standard Error is used as the threshold for defining an outlier point.

Metric 5:	The Kurtosis of the error distribution Qerror[]:

Where  is the standard deviation of the error set Qerror[]

The Kurtosis measures the relative spread of the model’s error distribution with respect to its standard deviation. The –3 term is classically introduced into the definition to compare the measured distribution to that of a normal distribution. A normal distribution has Kurtosis = 0, while a distribution with a shape broader than a normal distribution has a Kurtosis > 0.

### Metrics relating to agreement

Metric 6:	The Kappa coefficient.

=

Where ƒo is the observed number of agreement between MOS and MOSp for each of the 5 MOS class, and ƒE is the number of agreement due to coincidence (can be computed by the product of the number of MOS and MOSp for a given class, divided by N).

|  | MOS 1 | MOS 2 | MOS 3 | MOS 4 | MOS 5 | Total |
| --- | --- | --- | --- | --- | --- | --- |
| MOSp 1 | ƒo(1) |  |  |  |  | Tp 1 |
| MOSp 2 |  | ƒo(2) |  |  |  | Tp 2 |
| MOSp 3 |  |  | ƒo(3) |  |  | Tp 3 |
| MOSp 4 |  |  |  | ƒo(4) |  | Tp 4 |
| MOSp 5 |  |  |  |  | ƒo(5) | Tp 5 |
| Total | T 1 | T 2 | T 3 | T 4 | T 5 | N |

Where Ti = #MOSi and Tpi = #MOSpi.

and, ƒE(i)= (TiTpi)/N.

So, the Kappa is a metric of agreement, and is not influenced by coincidence. Thus, K values are between –1 and 1, but do not have to be interpreted as a correlation coefficient. K values are lower than correlation, and a value around 0.4 indicates that the method is efficient.

If these metrics will not allow model efficiency to be distinguished, it is possible to introduce a 7th metric as a false alarm rate. Indeed, it is possible to compute how many times the model gives a wrong estimation of the MOS class, and so on, to identify the most robust model.

## Generalizability

Generalizability is the ability of a model to perform reliably over a very broad range of video content. This is a critical selection factor given the very wide variety of content found in real applications. There is no specific metric that is specific to generalizability, so this objective testing procedure requires the selection of as broad a set of representative test sequences as is possible. The test sequences and specific HRC’s will be selected by the members of VQEG and should ensure broad coverage of typical content (spatial detail, motion complexity, color, etc.) and typical video processing conditions. The breadth of the test set will determine how well the generalizability of the models is tested. At least 20 different scenes are recommended as a minimum set of test sequences. It is suggested that some quantitative measures (e.g., criticality, spatial and temporal energy) should be used in the selection of the test sequences to verify the diversity of the test set.

## Complexity

The performance of a model as measured by the above Metrics #1-6 will be used as the primary basis for model recommendation. If several models are similar in performance, then the VQEG may choose to take model reference data bit rate into account in formulating their recommendations. For similar performance, the smaller reference data bit rate will be recommended. Thus, if reference data bitrates are not discriminating enough, a model comparison should be done within each module defined in ITU document 10-11Q/TEMP/28-R1.

# Calendar and actions

| Due date | Action | Who |
| --- | --- | --- |
|  | Test plan final version |  |
|  | Sequence processing |  |
|  | Subjective tests |  |
|  | Subjective data analysis |  |
|  | Submission of executable models |  |
|  | Objective data analysis Final report edition |  |
|  | Final report. |  |

# Recommendation

The VQEG will recommend methods of objective video quality assessment based on the primary evaluation metrics defined in Section 6. The Study Groups involved (ITU-T SG 12, ITU-T SG 9, and ITU-R SG 6) will make the final decision(s) on ITU Recommendations.

# Bibliography

- VQEG Phase I final report.

- VQEG Phase I Objective Test Plan.

- VQEG Phase I Subjective Test Plan.

- VQEG FR-TV Phase II Test Plan.

- Vector quantization and signal compression, by A. Gersho and R. M. Gray. Kluwer Academic Publisher, SECS159, 0-7923-9181-0.

- Recommendation ITU-R BT.500-10.

- document 10-11Q/TEMP/28-R1.

- RR/NR-TV Test Plan

# Annex: Optimum mean square quantization method.

The principal goal of quantizer design is to select the reproduction levels and the partition regions or cells so as to provide the minimum possible average distorsion for a fixed number of levels N (here N = 5). Effective algorithms are available, like the Lloyd one, which is proposed below. More explicitly, for the average (mean square) distorsion measure, the goal, as usually stated, is to find the output points yi and partition cells Ri that minimize

D =

Where ƒX is the pdf (probability density function) of the random variable X.

Specifically, the Lloyd algorithm is applied to the design of a quantizer for the empirical distribution, that is the distribution of the set of observations. Here, the set of observations is the MOS data set.

The key to this iterative algorithm is a mapping that converts a given codebook into a new and improved codebook. The design algorithm begins with an initial codebook and repeats this mapping until a suitable stopping criterion is satisfied. The codebook improvement mapping is the basic iteration of the algorithm.

## The Lloyd Iteration for codebook improvement

- Given a codebook Cm = {yi }, find the optimal partition into quantization cells, that is, use the nearest neighbor condition to form the nearest neighbor cells:

Ri = {x : d(x,yi)  d(x,yj); all j  i }

- Using the centroid (or center of mass) condition, find Cm+1, the optimal reproduction alphabet (codebook) for the cells just found.

The basic form of the Lloyd iteration assumes that the input pdf is known in order to compute the centroids (a sample distribution based on empirical observations is used instead of pdf to generate the improved codebook). Figure 2. Illustrates the Lloyd iteration and indicates the dependence of the mapping on the specified pdf.

Flow chart of the Lloyd iteration for codebook improvement

## The Lloyd algorithm

Step 1.	Begin with an initial codebook C1. Set m = 1.

Step 2.	Given the codebook, Cm, perform the Lloyd Iteration to generate the improved codebook Cm+1.

Step 3.	Compute the average distorsion for Cm+1. If it has changed by a small enough amount since the last iteration, stop. Otherwise set m+1  m and go to Step2.

The initial codebook may have the lattice pattern of a uniform quantizer or it may be a reasonable codebook that has N points roughly represent the range of values taken on by the input.

Annex I
Instructions to the Subjects

“In this test, we ask you to evaluate the overall quality of the video material you see.  We are interested in your opinion of the video quality of each scene.  Please do not base your opinion on the content of the scene or the quality of the acting.  Take into account the different aspects of the video quality and form your opinion based upon your total impression of the video quality.

Possible problems in quality include:

- poor, or inconsistent, reproduction of detail;

- poor reproduction of colours, brightness, or depth;

- poor reproduction of motion;

- imperfections, such as false patterns, or “snow”.

The test consists of a series of judgement trials. During each trial, two versions of a single video sequence, which may or may not differ in picture quality, will be shown in the following way:

“A” is the first version, “B” is the second version. The first presentation of a trial will be announced with the written caption “A”, and the second with “B”.  This pair of presentations will then be repeated, thereby completing a single trial.

In judging the overall quality of the presentations, we ask you to use judgement scales like the samples shown below.

# SAMPLE QUALITY SCALE

As you can see, there are two scales for each trial, one for the “A” presentation and one for the “B” presentation, since both the “A” and “B” presentations are to be judged.

The judgement scales are continuous vertical lines that are divided into five segments.  As a guide, the adjectives “excellent”, “good”, “fair”, “poor”, and “bad” have been aligned with the five segments of the scales.  You are asked to place a single horizontal line at the point on the scale that best corresponds to your judgement of the overall quality of the presentation (as shown in the example).

# You may make your mark at any point on the scale, which most precisely represents your judgement.

In making your judgements, we ask you to use the first pair of presentations in the trial to form an impression of the quality of each presentation, but to refrain from recording your judgements.  You may then use the second pair of presentations to confirm your first impressions and to record your judgements in your Response Booklet.

# We will now show you four demonstration trials.

DEMONSTRATION TRIALS PRESENTED AT THIS POINT

# Footnotes

Payment will be made directly from each proponent to the selected testing facility, according to a table agreed by ILG and distributed to the proponents.

# Text boxes

Nearest Neighbor Partitioning

Centroid Computation

Cm

Cm+1

1

Data set

3

post processing

2

evaluation metrics

4

Evaluation Metrics

5

Analysis

Final Report

Editors Note: unresolved issues or missing data are annotated by the string <<XXX>>