Margaret,

Yes, I think the method you propose is statistically valid if the 30 
sequences span the range of worst to best. That means that all the 
labs that introduce their own HRC-SRC combinations will have to 
choose them to fall within the quality range spanned by the 30 
sequences in your plan.

In FRTV2 I re-scaled each subject's data to a 0-1 scale before doing 
any other analysis. That got rid of variance that no model could be 
expected to handle -- i.e., made the data less noisy so all the 
models would fit better. That worked because each subject (at least 
within the 525 data) saw the same stimuli. In the current MM test 
plan, subjects in different labs will be seeing mainly different 
stimuli. Therefore, I won't know if re-scaling to 0-1 makes any sense 
-- unless each lab has the same stimulus range, which is bounded by 
the 30 common stimuli. If the labs do have the same set of 30 
boundary stimlui, then I will use them to scale each subject's 
responses to the 0-1 scale.

If we simply use the raw subjective data without any re-scaling to 
deal with individual differences in subjects, labs, and stimuli, all 
these effects on the data will get thrown into the residual error 
term. The error term will get big, and the fit of every model will 
suffer. In FRTV2 I was able to get rid of the effects of labs and 
subjects either by re-scaling or as part of the ANOVA analysis 
program -- by specifying, say, "lab" as an effect on the rating data, 
the effect of Lab is analytically removed from the error term. 
Therefore, all the fit measures like RMS error get better. In MM, 
the only way I see of getting this same kind of benefit is to use 
your 30-common-stimuli method, or something like it.

Greg

>Greg,
>
>My current understanding is that each subjective experiment will 
>have 200 video sequences, some of them processed and some them the 
>source sequences. Of these, 30 sequences will be identical in each 
>experiment at the same resolution (e., all VGA experiments). These 
>will be a complete matrix of 5 SRC and 5 HRC. With the 5 source 
>sequences, this totals 30 sequences.
>
>My proposal for aggregation was to take those common 25 processed 
>video sequences, and use those subjective scores to map the 
>subjective scores from different tests onto a single scale. The 
>mapping would be restricted to a linear mapping. The aggreggated 
>data would then be evaluated using the metrics in section 8 (I think 
>that is the right number); and the F-test could be used to 
>discriminate between models. Thus, this would give an overall 
>estimation of the model's performance on all video clips.
>
>We discussed the above idea yesterday. Some pe ople liked the idea, 
>some people did not. Mostly, the people who did not were uncertain 
>as to whether the above would be statistically valid. The idea was 
>dropped.
>
>If the above is clear, I would be interested in hearing your 
>opinion. Do you think the the above aggregation is valid?
>
>Margaret H Pinson, NTIA/ITS
>
>
>
>------ Original Message ------
>From: Greg Cermak <greg.cermak@verizon.com>
>Date: Thursday, September 29th, 2005 8:16 AM MDT
>To: margaret@its.bldrdoc.gov
>Subject: data aggregation
>
>Margaret,
>
>I'm not getting the point of your VQEG note on aggregating data in
>the MM Test ("Since VQEG has agreed to perform multiple tests on each
>image size, it seems to me that we should aggregate data. Otherwise,
>the data analysis will be too unwieldy. I suggest the
>following:...."). I'm not sure what part of it I'm not getting. My
>understanding is that each subjec t views and rates some number of
>video sequences. That number could be 50 or 500. My software just
>sees a string of trials for each of which there is a video identifier
>and a rating. The software doesn't care how long that string of
>trials is. It also doesn't care how many subjects there are.
>
>I expect that what I just wrote above is NOT what you had in mind in
>your note. What did you mean?
>
>Greg