| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 9 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | WD ?? |
|  | English only Original: English |
| Question(s): | 2,14/9 | Boulder, 25-29 January 2010 |
| TEMPORARY DOCUMENT |
| Source: | JRG-MMQA (VQEG) |
| Title: | Fast lossless compression of video data |

To develop video quality measurement methods, a large amount of data needs to be exchanged or transferred. As the video resolution increases, the file size also rapidly increases. For example, the average data size for a typical HD session (about 170 10s PVSs) is about 200G bytes. Although a number of compression programs are currently available, the encoding time can be long.

To exchange or transfer such a large amount of data, it would be helpful to use real-time lossless compression methods. Yonsei University developed a simple and fast lossless compression algorithm. The preliminary experiments showed promising results.

1. HD Session (YUV422)

The number of PVSs:	170

Average compression rate: 	40.74%

1) Compression performance per source

Table 1. Compression ratio per source (file size compared to the original).

| SRC01 | 47% |
| --- | --- |
| SRC02 | 44% |
| SRC03 | 38% |
| SRC04 | 34% |
| SRC05 | 38% |
| SRC06 | 37% |
| SRC07 | 43% |
| SRC08 | 46% |
| SRC09 | 44% |
| SRC10 | 36% |

Fig. 1. Compression ratio per source (file size compared to the original).

2) Compression performance per HRC

Table 2. Compression ratio per HRC (file size compared to the original).

| HRC00 | Source | 70% |
| --- | --- | --- |
| HRC01 | H025 | 56% |
| HRC02 | H025_E | 52% |
| HRC03 | H055 | 56% |
| HRC04 | H085 | 57% |
| HRC05 | H125 | 58% |
| HRC06 | H125_E | 54% |
| HRC07 | H165 | 59% |
| HRC08 | H195 | 60% |
| HRC09 | M035 | 50% |
| HRC10 | M035_E | 49% |
| HRC11 | M060 | 53% |
| HRC12 | M095 | 56% |
| HRC13 | M135 | 58% |
| HRC14 | M135_E | 58% |
| HRC15 | M175 | 59% |
| HRC16 | M215 | 60% |

Fig. 2. Compression ratio per HRC (file size compared to the original).