Multimedia 2

Detailed Description of Test Conditions

Version 1.0, June, 2012

Contacts:

Christian Schmidmer, OPTICOM GmbH, cs@opticom.de

Quan Huynh-Thu

Vittorio Baroncini

Editorial History

| Version | Date | Nature of the modification |
| --- | --- | --- |
| 1.0 | June 27, 2012 | Initial version, edited by C.Schmidmer |

Contents

1.	Introduction	5

2.	SRC Restrictions and Format	6

2.1	Video Material	6

2.1.1	Source Sequence Processing Overview and Restrictions	6

2.1.2	SRC Resolution, Frame Rate and Duration	6

2.1.3	Source Test Material Requirements: Quality, Camera, Use Restrictions.	6

2.1.4	Source Conversion	7

2.2	Audio Material	8

2.2.1	Format	8

2.2.2	Quality	8

2.2.3	Recording Equipment	8

2.3	File Format: Uncompressed AVI in UYVY	8

2.4	Source Sequence Documentation	9

2.5	Test Materials and Selection Criteria	9

3.	HRC Creation and Sequence Processing	11

3.1.1	Bit-Rates of Interest	11

3.2	Video Signals	11

3.2.1	Video Coding Schemes	11

3.2.2	Video Frame Rates (PVS)	11

3.2.3	Video Pre-Processing	12

3.2.4	Video Post-Processing	12

3.3	Audio	12

3.3.1	Audio Coding Schemes	12

3.3.2	Audio Bit-Rates (Examples)	12

3.3.3	Audio Sample Rates (PVS)	13

3.3.4	Audio Pre-Processing	13

3.3.5	Audio Post-Processing	13

3.4	Rebuffering	13

3.5	Transcoding	13

3.6	Transmission Errors	13

3.6.1	Simulated Transmission Errors	14

3.6.2	Live Network Conditions	15

3.7	Decoder Response to Transmission Errors and Player Impairments	16

3.8	PVS Editing	16

4.	Calibration and Registration	17

4.1	Constraints on PVS (e.g., Calibration and Registration)	17

# Introduction

This document contains a description of the format of source sequences to be used for the VQEG MM2 project, the HRC requirements and the allowed limits for the final processed video sequences. This document includes information important to model developers as well as independent test labs.

If not otherwise stated, all everything described in this document is binding for proponents, ILGs and test labs.

A summary of the VQEG MM2 project as well as a description of the available documents and their current versions is contained in the document “VQEG_MM_2012_xxx_V1.0_MM2_Project_Synopsis.doc”.

# Target Applications

The objective of the MM2 project is to validate objective methods for the assessment of the combined audio-visual quality from an end users perspective. Targeted scenarios include, but are not limited to broadcast and streaming of audio-visual sequences over fixed and mobile networks, with a focus on consumer entertainment. The objective models are meant to be applied to short sequences (app. 10s) only.

# SRC Restrictions and Format

## Video Material

### Source Sequence Processing Overview and Restrictions

The test material will be selected from a common pool of video sequences.

The source video can only be used in the testing if an expert in the field considers the quality to be good or excellent on an ACR-scale. The source video should have no visible coding artifacts. The final decision whether a source video sequence is admissible will be made by ILGs.

The source video should have no visible coding artifacts. 1080i footage may be de-interlaced and then used as SRC in a 1080p experiment. 1080p enlarged from 720p or 1080i enlarged from 1366x768 or similar are valid source sequences. 1080p 24fps film footage can be converted and used in any 1080i or 1080p experiment. Otherwise, the frame rate of the unconverted source must be at least as high as the target SRC (e.g., 720p 50fps can be converted and used in a 1080i 50fps experiment, but 720p 29.97fps cannot be converted and used in a 1080i 59.94fps experiment).

Uncompressed AVI files will be used for subjective and objective tests. The progressive test sequences used in the subjective tests should also be used by the models to produce objective scores. Note that the subjective playback system must introduce no additional visual impairments. It is important to minimize the processing of video source sequences. Hence, we will endeavor to find methods that minimize this processing (e.g., to perform de-interlacing and resizing in one step).

### SRC Resolution, Frame Rate and Duration

The length of the source sequence depends upon the resolution, as follows.  Note that the duration of VGA source sequences depends upon whether or not rebuffering will be considered in the experiment. (Note: rebuffering is defined as a pausing without skipping (aka frame freeze) event that lasts for more than 0.5 seconds.)

| Resolution | Raw SRC for Coding | Edited SRC & PVS |
| --- | --- | --- |
| HD | 14 seconds | 10 seconds |

The original source (before editing) must include an extra 2 seconds at the beginning and the end!

### Source Test Material Requirements: Quality, Camera, Use Restrictions.

HD source test material should be taken from a professional grade HD camera (e.g., Sony HDR-FX1) or better. Video quality obtained by using a professional grade DSLR is generally excellent, but filming with a DSLR typically requires good skills of the videographer and often special, expensive lenses (lenses for still photography often do not allow smooth changes of aperture and focus. Special rigs may overcome this limitation).

Note 1: The source video will only be used in the testing if an expert in the field considers the quality to be good or excellent on an ACR-scale.

### Source Conversion

This section describes approved methods for converting source video from one format to another used in this experiment. These tools are known to operate correctly.

#### Software Tools

Transformation of the source test sequences (e.g., from Rec. 720p to VGA) shall be performed using Avisynth 2.5.5 or later and the most recent version of VirtualDub. Within VirtualDub, video sequences will be saved to AVI files by specifying the appropriate color space for both read and write (Video ( Color Depth), then selecting Video Compression option (Video ( Compressor) to be "Uncompressed RGB/YCbCr". For the Colour Depth “4:2:2 YCbCr (UYVY)” is used as output format. The processing mode (Video () is set to “Full processing mode”.

#### Colour Space Conversion

In the absence of known color transformation matrices (e.g., such as what might be used by a video display adapter), the following algorithms will be used to transform between ITU-R Recommendation BT.601 Y'CB'CR' video and R'G'B' video that is in the range [0, 255].  The reference for these color transformation equations is pages 15-16 of ColorFAQ.pdf, which can be downloaded from:

http://www.poynton.com/PDFs/ColorFAQ.pdf

Transforming R'G'B' to Y'CB'CR'

1.  Compute the matrix transformation:

2.  Round to the nearest integer.

3.  Clamp all three components to the range 1 through 254 inclusive (0 and 255 are reserved for synchronization signals in ITU-R Recommendation BT.601).

Transforming Y'CB'CR' to R'G'B'

1.  Compute the matrix transformation:

2.  Round to the nearest integer.

3.  Clamp all three components to the range 0 through 255 inclusive.

#### De-Interlacing

De-interlacing will be performed when original material is interlaced and requires de-interlacing, using the de-interlacing function “KernelDeint” in Avisynth. If the de-interlacing using KernelDeint results in a source sequence that has serious artifacts, the Blendfield or Autodeint may be used as alternative methods for de-interlacing. Proprietary algorithms and/or hardware de-interlacing may be used if the above three methods prove unsatisfactory.

To check for de-interlacing problems (e.g. serious artifacts introduced by the de-interlacing process), the source content will be played back at normal speed, with the option to inspect possible problems at reduced speed.

#### Cropping & Rescaling

No cropping or rescaling shall be used.

Note: for hybrid we needed this section since HD videos had to be scaled to WVGA. How is that for HD?

## Audio Material

### Format

All audio material must be available in 16 bit linear PCM resolution and at a sample rate of either 44.1 KHz or 48 kHz.

### Quality

The quality of the audio recordings will be judged by experts. It must score at least 4.0 on a five point ACR scale. The final decision if material is acceptable or not is up to an independent lab group.

### Recording Equipment

The built in microphones of most cameras are typically not of sufficiently high quality to fulfill the criteria specified for audio signals in this document! The usage of good, external microphones is recommended, also to avoid recording of sounds produced by the camera itself. Care must be taken, that the recorded signals are not significantly compressed, since tandeming audio codecs generally leads to sever degradations. The recording equipment must meet the following criteria:

THD+N:	X dB

SNR:	X dB

Frequency response: 	20Hz-20kHz

As an alternative to recording sound with the video signals, audio and video tracks may be mixed offline, using e.g. Adobe Premiere. In this case, other audio sources like e.g. CDs may be used as long as the copyright permits this use.

## File Format: Uncompressed AVI in UYVY

AUDIO FORMAT IS STILL MISSING!

All source and processed video sequences will be stored in Uncompressed AVI in UyVy..

Source material with a source frame rate of 29.97 fps will be manually assigned a source frame rate of 30 fps prior to being inserted into the common pool of video sequences (is this correct for HD?).

AVI is essentially a container format that consists of hierarchical chunks – which have their equivalent in C data structures – which are all preceded by a so called fourcc, a “four character code”, which indicates the type of chunk following. Some of the chunks are compulsory and describe the structure of the file, while some are optional and others contain the real video or audio data. The AVI container format which is used for the exchange of files in VQEG is originally defined by Microsoft as part of the RIFF file specification in:

“http://msdn.microsoft.com/library/default.asp?url=/library/en-us/wcedshow/html/_dxce_dshow_avi_riff_file_reference.asp”

Other descriptions can be found in:

http://www.opennet.ru/docs/formats/avi.txt

http://www.the-labs.com/Video/odmlff2-avidef.pdf

A description of the UYVY chunk format which is to be used inside the AVI container can be found in http://www.fourcc.org/index.php?http%3A//www.fourcc.org/fccyvrgb.php and below.

UYVY is a YUV 4:2:2 format. The effective bits per pixel are 16. In the AVI main header (after the fourcc “avih”), a positive height parameter implies a top-down image (top line first).Two image pixels form one macro pixel and are stored in one 32bit word with the following byte ordering:

(lowest byte) U0 Y0 V0 Y1 (highest byte)

## Source Sequence Documentation

Preferably, each source video sequence should be documented.  The exact process used to create each source video sequence should be documented, listing the following information:

Camera specifications

Recording equipment specification

Use restrictions (e.g., “open source”)

De-interlacing method (if used)

Any compression and post-processing applied

This documentation is desirable but not required.

## Test Materials and Selection Criteria

The test material will be representative of a range of content and applications. The list below identifies the type of test material that forms the basis for selection of sequences.

VQEG expresses a preference for all test material to be open source. At a minimum, source material must be available within the VQEG MM2 project to both proponents and ILG for testing (e.g., under non-disclosure agreement if necessary).

The SRCS used in each experiment must cover a variety of content categories from this list. At least 6 categories of content are recommended to be included in each experiment, if possible.

1)	video conferencing:

available for research purposes only, NTIA (Rec 601 60Hz); BT (Rec 601 50Hz), Yonsei (VGA), FT (Rec 601 50Hz, D1)), NTT (Rec 601 60Hz, D1)

Currently available: NTIA, NTT, FT

2)	movies, movie trailers:

(VQEG Phase II), Opticom, IRCCyN, (trailer equivalent, restricted within VQEG)

Currently available: Psytechnics, SVT, Opticom,

3)	sports

available, 15-20 mins from Yonsei, Comcast), KDDI (7 min D1 and D2, other scenes also available), NTIA (Comcast), IRCCyN

Currently available: Yonsei, SVT, Psytechnics, Opticom

4)	music video

(Intel ), IRCCyN

Currently available: NTIA

5)	advertisement:

Currently available: Psytechnics, Opticom

6)	animation:

graphics Phase I, cartoon Phase II; Opticom will send material to Yonsei), IRCCyN

Currently available: Opticom, NTIA

7)	broadcasting news

head and shoulders and outside broadcasting). (available – Yonsei;, possible Comcast), IRCCyN

Currently available: KBS, Opticom

- home video

FUB possibly, BT possibly, INTEL, NTIA). Must be captured with DV camera or better.

Currently available: NTIA, SwissQual, Yonsei

There will be no completely still video scenes in the test.

All test material should be sent to the content point of contact (Chulhee Lee, Yonsei) first and then it will be put on the ftp server by NTIA. Ideally the material should be converted before being sent to Chulhee Lee.

The ILG is responsible for selecting SRC material to be used in each subjective quality test.

# HRC Creation and Sequence Processing

The subjective tests will be performed to investigate a range of Hypothetical Reference Circuit (HRC) error conditions. These error conditions may include, but will not be limited to, the following:

- Compression errors (such as those introduced by varying bit-rate, codec type, frame rate and so on)

- Transmission errors

- Post-processing effects

- Live network conditions

- Interlacing problems

- AV Synch

The overall selection of the HRCs will be done such that most, but not necessarily all, of the following conditions are represented.

### Bit-Rates of Interest

The combined, average audio and video bitrate shall be in a range between 1Mbit/s to 30Mbit/s.

## Video Signals

### Video Coding Schemes

H.264

### Video Frame Rates (PVS)

For those codecs that only offer automatically set frame rate, this rate will be decided by the codec. Some codecs will have options to set the frame rate either automatically or manually. For those codecs that have options for manually setting the frame rate (and we choose to set it for the particular case) manually set frame rates (constant frame rate) may include:

- HDTV:	Manual reduction of frame rate is allowed

For codecs that offer variable frame rate encoding, variable frame rates are acceptable for VGA HRCs only.

Care must be taken when creating test sequences for display on a PC monitor. The refresh rate can influence the reproduction quality of the video and VQEG Hybrid requires that the sampling rate and display output rate are compatible.

The intended frame rate of the source and the PVS must be identical

Proposed new wording (instead of entire section above):

The HRC may create videos with frame rates between 5 fps and 60 fps. Variable as well as constant frame rates are allowed. For simplicity and to avoid problems with uncontrolled behavior of monitors used in subjective tests, the final PVS will be resampled to 25i, 30i, 50p or 60p. In any case, the PVS must have the same frame rate as the associated SRC has.

For example: given a source frame rate of video is 30fps, the sampling rate is 30/X (e.g.  30/2 = sampling rate of 15fps). This is called frame rate. Then we upsample and repeat frames from the sampling rate of 15fps to obtain 30 fps for display output.

### Video Pre-Processing

The HRC processing may include, typically prior to the encoding, one or more of the following:

- Filtering

- Colour space conversion (e.g. from 4:2:2 to 4:2:0)

- Down- and up-sampling (e.g., 1920x1080 down-sampled to 960x1080, transmitted, then up-sampled back to 1920x1080, and thus the bit-stream contains a resolution different than that shown to the viewer)

This processing will be considered part of the HRC.

### Video Post-Processing

The following post-processing effects may be used in the preparation of test material:

- Colour space conversion

- De-blocking

- Decoder jitter (what is that????)

- Down- and up-sampling (e.g., 1920x1080 down-sampled to 960x1080, transmitted, then up-sampled back to 1920x1080, and thus the bit-stream contains a resolution different than that shown to the viewer)

## Audio

### Audio Coding Schemes

Audio codecs included with an HRC may comprise MP3, AAC, HE-AAC, WMA, Dolby Digital, HILN. Speech codecs like AMR or EVRC are acceptable for voice only applications. Other codecs are acceptable as long as they are widely used in real life or likely to be frequently used in the near future.

### Audio Bit-Rates (Examples)

Audio bit rates to be considered should cover he range between 8 Kbit/s and 256 Kbit/s. The worst audio quality should not be less than the equivalent of 8 Kbit/s MP3.

Note: At 256 Kbit/s most current audio codecs will deliver near transparent quality (equivalent to CD).

### Audio Sample Rates (PVS)

Allowed sample rates of the PVS are 44.1 KHz and 48 KHz. In any case the sample rate of the PVS must match the sample rate of the SRC. To achieve this, up-sampling from any lower sample rate is allowed, if the codec used in the HRC produces signals with lower sample rates.

Clock drifts between the sample rate of the SRC and the PVS lower than 2% are allowed. Such drifts occur in real life by using analog equipment with unsynchronized clocks of the D/A and A/D converters, or if sample rate converters are used to match studio clocks with world clocks.

Note: Some consumer audio equipment might not be suitable for the reproduction of 48 KHz content.

### Audio Pre-Processing

Linear filtering of the audio signals is allowed and seen as part of the HRC.

Dynamic range compression is not allowed.

Sample rate conversions are allowed.

### Audio Post-Processing

Linear filtering of the audio signals is allowed and seen as part of the HRC.

Dynamic range compression is not allowed.

Sample rate conversions are allowed.

## Rebuffering

Rebuffereing of up to XXX % of the total duration (including the rebuffering section) is allowed within each PVS. During rebuffering, no extra information that was not present in the SRC must be visible / audible in the final PVS (e.g. no spinning wheel).

## Transcoding

Transcoding is allowed (e.g., an HRC was encoded at one bit rate and then re-encode at a higher bit-rate). No transmission errors may occur before the final transcoding. Thus, all transmission errors will be captured in the bit-stream. Transcoding should be realistic.

## Transmission Errors

Any transmission errors will be allowed as long as the corresponding PVSs meet the calibration limits given in section xxx and as long as they are realistic for a real world transmission chain.

The “Simulated Transmission Errors” and “Live Network Conditions” sub-sections provide guidance on transmission error HRC creation.

If the final transport is packet based, it is strongly recommended to also capture a PCAP file for later reuse of the data (SRC, PVS and PCAP file) with a hybrid model.

### Simulated Transmission Errors

The text below must be adapted to MM II!

A set of test conditions (HRC) will include error profiles and levels representative of video transmission over different types of transport bearers:

- Packet-switched transport (e.g., 2G or 3G mobile video streaming, PC-based wireline video streaming)

- Circuit-switched transport (e.g., mobile video-telephony)

- IPTV

- VoD

It is important that when creating HRCs by using a simulator, documentation is produced which details the simulator settings (for circuit switched HRCs the error pattern for each PVS should also be produced).

Packet-switched transmission

HRCs will include packet loss with a range of packet loss ratios (PLR) representative of typical real-life scenarios.

In mobile video streaming, we consider the following scenarios:

- Arrival of packets is delayed due to re-transmission over the air. Re-transmission is requested either because packets are corrupted when being transmitted over the air, or because of network congestion on the fixed IP part. Video will play until the buffer empties if no new (error-checked/corrected) packet is received. If the video buffer empties, the video will pause until a sufficient number of packets are buffered again. This means that in the case of heavy network congestion or bad radio conditions, video will pause without skipping during re-buffering, and no video frames will be lost.

- Arrival of packets is delayed, and the delay is too large: These packets are discarded by the video client.

Note: A radio link normally has in-order delivery, which means that if one packet is delayed the following packets will also be delayed.

Note: If the packet delay is too long, the radio network might drop the packet.

- Very bad radio conditions: Massive packet loss occurs.

- Handovers: Packet loss can be caused by handovers. Packets are lost in bursts and cause image artifacts.

Note: This is valid only for certain radio networks and radio links, like GSM or HSDPA in WCDMA. A dedicated radio channel in WCDMA uses soft handover, which will not cause any packet loss.

Typical radio network error conditions are:

- Packet delays between 100 ms and 5 seconds.

In PC-based wireline video streaming, network congestion causes packet loss during IP transmission.

In order to cover different scenarios, we consider the following models of packet loss:

- Bursty packet loss. The packet loss pattern can be generated by a link simulator or by a bit or block error model, such as the Gilbert-Elliott model.

- Random packet loss

- Periodic packet loss.

Note: The bursty loss model is probably the most common scenario in a ‘normal’ network operation. However, periodic or random packet loss can be caused by a faulty piece of equipment in the network.  Bursty, random, and periodic packet loss models are available in commercially-available packet network emulators.

Choice of a specific PLR is not sufficient to characterize packet loss effects, as perceived quality will also be dependent on codecs, content, packet loss distribution (profiles) and which types of video frames were hit by the loss of packets. For our tests, we will select different levels of loss ratio with different distribution profiles in order to produce test material that spreads over a wide range of audio-visual quality To confirm that test files do cover a wide range of quality, the generated test files (i.e., PVS after simulation of transmission error) will be:

- Rated by experts to ensure that the degradations resulting from the simulated transmission error are spread over a range of quality over different content;

- Checked to ensure that degradations remain within the limits stated by the test plan (e.g., in the case where packet loss causes loss of complete frames, we will check that temporal misalignment remains within the limits stated by the test plan).

NOTE: Circuit switched transmission section has been deleted!

### Live Network Conditions

Simulated errors are an excellent means to test the behavior of a system under well-defined conditions and to observe the effects of isolated distortions. In real live networks however usually a multitude of effects happen simultaneously when signals are transmitted, especially when radio interfaces are involved. Some effects like e.g. handovers can only be observed in live networks.

The term "live network" specifies conditions which make use of a real network for the signal transmission. This network is not exclusively used by the test setup. It does not mean that the recorded data themselves are taken from live traffic in the sense of passive network monitoring. The recordings may be generated by traditional intrusive test tools, but the network itself must not be simulated.

Live network conditions of interest include radio transmission (e.g., mobile applications) and fixed IP transmission (e.g., PC-based audio-visual streaming, PC to PC video-conferencing, best-effort IP-network with ADSL-access).  Live network testing conditions are of particular value for conditions that cannot confidently be generated by network simulated transmission errors. Live network conditions should exhibit distortions representative of real-world situations that remain within the limits stated elsewhere in this document.

Normally most live network samples are of as good quality as the underlying technology permits and no big differences between different samples can be observed under stationary conditions. To get a good proportion of sample quality levels, an even distribution of samples from high to low quality should be saved after a live network sessions.

Note: Keep in mind the characteristics of the radio network used in the test. Some networks will be able to keep a very good radio link quality until it suddenly drops. Others will make the quality to slowly degrade.

Samples with perfect quality do not need to be taken from live network conditions. They can instead be recorded from simulation tests.

Live network conditions as opposed to simulated errors are typically very uncontrolled by their nature. The distortion types that may appear are generally very unpredictable. However, they represent the most realistic conditions as observed by users of e.g. 3G networks.

Recording PVSs under live network conditions is generally a challenging task since a real hardware test setup is required.  Ideally, the capture method should not introduce any further degradation.  The only requirement on the capture method is that the captured sequences conform to the video file requirements.

For applications including radio transmissions, one possibility is to use a laptop with e.g. a built-in 3G network card and to download streams from a server through a radio network. Another possibility is the use of drive test tools and to simulate a similar download while the car is driving. In order to simulate very bad radio coverage, the antenna may be wrapped with some aluminum foil (Editors note: Strictly, this is a simulation again, but for the sake of simplicity it can be accepted since the simulated bad coverage is overlaid with the effects from the live network).

In order to prepare the PVSs the same rules apply as for simulated network conditions. The only difference is the network used for the transmission.

## Decoder Response to Transmission Errors and Player Impairments

Forward error correction (FEC) is not allowed (why??).  The decoder may request retransmission of packets or any other behavior allowed by other portions of this test plan (e.g., calibration limits, standard decoder).

Impairments coming from decoder are allowed and seen as part of the HRC. The decoder (player) settings should be realistic. For example, a very small buffer should not be used for HDTV. The recorded PVS has to conform to the calibration limits in section XX.

## PVS Editing

The edited PVS must have the following duration:

| Video Resolution | Duration of Edited SRC and PVS |
| --- | --- |
| HD, no Rebuffering | SRC must be 15 seconds Edited PVS must be between 15 and 23 seconds duration. An average duration of 19 seconds is recommended (check with latest hybrid test plan!) |

# Calibration and Registration

## Constraints on PVS (e.g., Calibration and Registration)

The following constraints must be met by every PVS.  These constraints were chosen to be easily checked and to provide proponents with feedback on their model's calibration intended search range

| Factor | Limitation | Other Details |
| --- | --- | --- |
| Luminance Gain | Maximum ± 20% |  |
| Luminance Offset | Maximum ± 50 |  |
| Horizontal Shift | HD Maximum ± 16 pixels |  |
| Vertical Shift | Maximum ± 5 lines |  |
| Spatial Scaling | No visibly obvious scaling |  |
| Color Space | Must appear correct | For example, a red apple should not mistakenly rendered be rendered "blue" due to a swap of the Cb and Cr color planes. |
| Frozen Frames & Pure Uni-Color Frames | No more than ½ of a PVS. | For example, from over-the-air broadcast lack of delivery. |
| First 2-sec and last 2-sec of edited PVS | May not contain pure uni-color frames. | The reason for this constraint is that the viewers may be confused and mistake the uni-color for the end of sequence. |
| Field Order | Field order must not be swapped | For example, field one moved forward in time into field two, field two moved back in time into field one. |
| SRC Video Pre-Roll | When creating PVSs, a SRC with +2 second of extra content before and after should be used. | These ±2sec pre-roll will typically not be visible within the edited PVS. The intention is that the PVS matches the SRC without this ± 2sec pre-roll. |
| Total Extra Frames | All of the content visible in the edited PVS must be contained within the SRC plus ± 2sec pre-roll. | Recommend ≤ 1 second |
| Total Frame Loss This includes both the beginning and the end. Thus, total frame loss = maximum frame loss at start + maximum frame loss at end. | Maximum 2 seconds | Recommend ≤ 1 second |
| Each Rebuffering Event (pausing without skipping) | From 0.5 sec, up to 50% of the SRC length | Recommend ≤ 3 seconds |
| Each Skipping Event | Maximum 5 seconds skipped | Recommend ≤ 3 seconds |
| First 1-sec and last 1-sec of edited PVS | Must contain at least four unique frames, provided the source content is not still for those seconds. |  |
| AV Synchronization | Max +/-1 s |  |
| Audio Delay Variation | +/- 500 ms | Related to sporadic, sudden changes of the delay |
| Audio Clock Drift | <= +/-1% relative to the SRC | Related to continuous, smooth delay changes. |
| Audio Delay | +/-2s | Where is the reference point? After the preroll? |
| Video Delay | +/-2s | Where is the reference point? After the preroll? |

Note that “Total Frame Loss” and “Total Extra Frames” refer to the duration of the edited PVS. Anything can happen in-between (freezing with/without skipping, skipping, fast forward) as long as they meet the aforementioned conditions. The video should not play backwards, because this is an unnatural impairment.  However, the video may jump backwards in time in response to a transmission error, or display a portion of a previous frame along with the current frame.

Figure 1 shows three examples of total lost frames for a VGA test with no rebuffering.  The edited SRC and PVS are 10sec duration. The SRC are shown with the 2sec preroll before and after (i.e., beyond the dotted line). The arrows indicate the time alignment of the first and last frame of the PVS, with matching colors indicating where the PVS content matches the SRC content. In the top example, frames are lost from at the end of the edited PVS; in the middle example, frames are lost at the beginning of the edited PVS, and in the bottom example, frames are lost from both the beginning and the end.

Similarly, figure Figure 2 shows three examples of total extra frames for a VGA test with no rebuffering.

The loss or extra frames at both the beginning and end of the PVS must be considered (e.g., the bottom examples of Figure 1 and Figure 2)

If possible, the beginning of the source and the beginning of the PVS should be aligned.

Figure 1, total frame loss, shown for 10 s SRC and PVS without rebuffering.

Figure 2, total extra frames, shown for 10 s SRC and PVS without rebuffering.

The intent of this test plan, is that all PVSs will contain realistic impairments that could be encountered in real delivery of HDTV (e.g., over-the-air broadcast, satellite, cable, IPTV).  If a PVS appears to be completely unrealistic, proponents or ILGs may request to remove or replace it. ILGs will make the final decision regarding the removal or replacement.

Calibration checks will only be performed on the portions of PVSs that are not anomalously severely distorted (e.g. in the case of transmission errors or codec errors due to malfunction).

# Text boxes

PVS, Loss at End

PVS, Loss at Beginning

PVS, Loss at Both Ends

2sec Preroll

2sec Preroll

2sec Preroll

2sec Preroll

2sec Preroll

2sec Preroll

SRC

SRC

SRC

10sec

PVS, Extra Frames at Beginning

PVS, Extra Frames at Both Ends

2sec Preroll

2sec Preroll

SRC

SRC

SRC

10sec

2sec Preroll

PVS, Extra Frames at End

2sec Preroll

2sec Preroll

2sec Preroll