| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 9 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2013-2016 | TD 110 (GEN/9) |
|  | English only Original: English |
| Question(s): | 2/9 | Geneva 14 – 18 January 2013 |
| TEMPORARY DOCUMENT |
| Source: | Editors J.3D-disp-req |
| Title: | Output - Draft New Recommendation J.3D-disp-req “Display requirements for 3D video quality assessment” |

-------------

Editor Note: This document represents the output from Q2/9 sessions during SG 9 meeting, 14 – 18 January 2013. It provides revisions based on the previous TD 848 (GEN/9 of the previous Study Period).

----------------

<Recommendation No.>

Draft New Recommendation J.3D-disp-req: Display Requirements for 3D Video Quality Assessment

Summary

This recommendation specifies the requirements for the selection of 3D displays when conducting subjective quality assessment experiments.

Keywords

<Optional>

Introduction

<Optional - This clause should appear only if it contains information different from Scope and Summary>

# 1	Scope

This Recommendation provides guidelines on the display selection and on the display requirements for 3D video quality assessment. Compared to 2D video, several new issues have arisen in 3D video applications. Compared to 2D video, 3D display technologies still face some challenges. It is therefore important to take into account the potential sub-optimal rendering of the 3D display when assessing the 3D viewing experience. It is also important to characterize and report properly the 3D display characteristics in the context of subjective testing as this information helps in interpreting correctly subjective results. In particular, 3DTVs exhibit crosstalk to various degrees and can impact negatively the viewing experience.Crosstalk is a major factor in video quality, visual discomfort and visual fatigue problems. This recommendation provides guidelines for the selection of 3D displays for consistent and repeatable subjective video quality assessment.

## 1.1	Applications

The applications for the 3D display requirements described in this Recommendation include, but are not limited to:

- Minimum requirements for 3D display in the context of subjective quality assessment of 3D video;

- Consistent and repeatable quality assessment of 3D video sequences.

## 1.2	Limitations

This Recommendation only applies to video quality assessment of coding and transmission error scenarios where the 3D video sequences are moderately to strongly degraded. More stringent display requirements may be needed to accurately assess quality in the presence of nearly lossless quality impairments (e.g., where the quality is nearly the same as the original 3D video).

# 2	References

# Normative References

# Informative References

[ITU-T P.910] ITU-T Recommendation P.910 (2008), Subjective video quality assessment methods or multimedia applications.

[ITU-T P.911] ITU-T Recommendation P.911 (1998), Subjective audiovisual quality assessment methods for multimedia applications.

# [IDMS1] International Committee for Display Metrology (ICDM)  (2012), Information Display Measurement Standard

# 3	Definitions

This recommendation uses the following terms defined elsewhere.

## 3.1	Terms defined elsewhere:

This Recommendation uses the following terms defined elsewhere:

3.1.1

3.1.2

## 3.2	Terms defined in this Recommendation

This Recommendation defines the following terms:

3.2.1

3.2.2

# 4	Abbreviations and acronyms

This Recommendation uses the following abbreviations and acronyms:

# 5	Conventions

None.

# 6	3D Display Requirements

## 6.1 Crosstalk

- Effects of crosstalk on 3D video quality assessment

In the context of subjective quality assessment of 3D video, a suitable 3D display must be selected such that the display does not affect the reliability and reproducibility of subjective results. However, crosstalk is a major contributor to quality loss and visual discomfort on stereoscopic displays. It can therefore greatly impact the quality of experience in the viewing of stereoscopic 3D content and the results of subjective quality assessment.

To achieve consistent results of 3D video quality assessment, it is important to understand the maximum amount of allowable display crosstalk.  Subjective testing requires  measurement or characterization means to adequately select display equipment to conduct such subjective testing in a reliable and repeatable manner.

Several works in the literature and works presented to the Video Quality Experts Group have shown that objective physical measurements of 3D displays to characterize their crosstalk is not straightforward and repeatability of results is still an issue to solve. There are many parameters (e.g., distance, angle, characteristics of the measurement instruments) that make physical measurements difficult and many aspects (e.g., non-uniformity, spatial/temporal variation, anti-crosstalk mechanisms) that make crosstalk difficult to represent as a single value.

Note: Because of the problems mentioned above, a proposed alternative approach to characterize the impact of the display crosstalk on perceived 3D visual experience is the use of subjective testing where participants are asked to perform a disparity discrimination task, with the idea that the accuracy of the subjects responses will be negatively impacted by the display crosstalk. Further experiments are necessary to examine the merits of such approach, how it compares to physical measurements, and how such task recognition accuracy may be considered as a potential criterion for 3D display selection.

## 6.2 Crosstalk measurements

### 6.2.1 Grey-to-grey crosstalk

Crosstalk is not necessarily only due to leakage of unintended white image/level onto intended black image/level but also to other grey-to-grey configurations (other grey-to-grey configurations may produce as perceivable/visible crosstalk)

The selection of a 3D display for subjective quality assessment of 3D content should not be based only on the measure of crosstalk using the leakage of light signal from the open to the blocked channel, using a white image as the open channel signal and a black image as blocked channel signal but should also consider the following aspects:

1. The spatial variation of the crosstalk

2. The angular variation of the crosstalk (crosstalk off the center axis)

3. Chromatic aspects

### 6.2.2 Angular influence

Two angular influences must be taken into account:

- A spatial measurement can record crosstalk variation depending on the eye gaze direction (e.g. position in the image). This gives already an angular indication of how the angular dependence of the Liquid Crystal Shutter and the display angular emission are combined. In the case of LCD displays, light polarization and its interaction with the glasses polarization analyzers create specific effects altering image and crosstalk homogeneity.

- Another angular variation depends on the observer’s position in front of the screen. The same effects of direction dependent light emission and of interaction between screen emission and glasses analysis will happen.

Because of the two points mentioned above, crosstalk measured at a specific angle can be dramatically more significant than a basic central measure on the screen normal axis. A single measurement at the centre of the screen is therefore not sufficient.

______________